EE236 : Quiz 1
Mayur Ware | 19D070070
Observations :
Q1)
Transfer Characterirstics of both are almost similar but full wave rectifier has a smooth waveform whereas precision rectifier waveform in not smooth and it is repeatadly following the same path where sometimes it’s getting unregular.

Q2)
Diode X :
In log graph,
x0= 0.26, y0=-7.7931
x1=0.127, y1=-11.6552
Slope = 29.2291
y-intercept = -15.5

So,
Ideality factor (eta) = 1.3159
Saturation Current (Is) = 0.186uA
Peak Inverse Voltage = -75V
Forward Voltage = 0.3V

Diode Y :
In log graph,
x0= 0.4618, y0=-11
x1=0.2813, y1=-15.80
Slope = 26.63
y-intercept = -23.6

So,
Ideality factor (eta) = 1.444
Saturation Current (Is) = 5.63e-11 A
Peak Inverse Voltage = -1000V
Forward Voltage = 0.6V

Diode X can be used in rectifiers instead of Y as it’s forward bias voltage is low as compared to Y